## Slide 1: 미래차 부트캠프 On-device AI
Lecture 6: Polling and Interrupt
Jong Hwan Ko
Associate Professor
SungKyunKwan University, Korea
Department of Electrical and Computer Engineering
jhko@skku.edu

## Slide 2: 7. Mapping & Dataflow
Mapping onto Hardware
DLA
(Deep Learning Accelerator)
MAPPING
Loop reordering
Loop tiling
Loop unrolling
Vectorization
Edge-host partitioning
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 3: 7. Mapping & Dataflow
ML Compiler
source: sampl.cs.washington.edu/projects/tvm.html

## Slide 4: 7. Mapping & Dataflow
Motivation: Memory Hierarchy
Operation | Precision | Energy (pJ)
Addition | INT8 | 0.03
 | INT16 | 0.05
 | INT32 | 0.1
 | FP16 | 0.4
 | FP32 | 0.9
Multiplication | INT8 | 0.2
 | INT32 | 3.1
 | FP16 | 1.1
 | FP32 | 3.7
32-bit SRAM Read (8 kB) |  | 5
32-bit SRAM Read (32 kB) |  | 10
32-bit SRAM Read (1 MB) |  | 100
32-bit DRAM Read |  | 640
Adapted from Mark Horowitz “Computing’s Energy Problem (and What we can do about it)” ISSCC 2014
Relative Energy Cost (Log-scale)
Memory is the issue!

## Slide 5: 7. Mapping & Dataflow
Get data close to the computation. (LOCALITY)
Once data is close - perform all computations with this data. (REUSE)
Operation |  | Energy (pJ)
32-bit SRAM Read (8 kB) |  | 5
32-bit SRAM Read (32 kB) |  | 10
32-bit SRAM Read (1 MB) |  | 100
32-bit DRAM Read |  | 640
Relative Energy Cost (Log-scale)
Motivation: Memory Hierarchy
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 6: 7. Mapping & Dataflow
Why do we have a memory hierarchy?
  The closer you get to compute, the more $$ and scarce the memory resource becomes
  In most cases, the DNN parameters live off chip and are fetched layer-by-layer or tile-by-tile
  Data locality: how to get data close to the PEs (to keep them fully utilized)
Accelerator Chip
PE
External Memory
Main Memory
Global Memory
Off-Chip Memory
DRAM / HBM
Shared Memory
Cache
On-Chip Buffer
On-Chip Memory
SRAM
Register File
Private memory
GB
MB
KB
Local Memory
Motivation: Memory Hierarchy
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 7: 7. Mapping & Dataflow
Motivation: Memory Hierarchy
Adapted from “TinyML and Efficient Deep Learning Computing” Lecture (Fall 2024) by Prof. Song Han (MIT)

## Slide 8: 7. Mapping & Dataflow
Motivation: Data Reuse
Temporal Reuse
Read once from memory, use same data multiple times by same PE
Memory
PE
x
Spatial Reuse
Read once from memory, use same data multiple times by multiple PEs
Memory
PE
x
PE
x
PE
x
3
1
2
5
Reuse entry multiple times from a single memory read
3
3
3
Reuse entry multiple times from a single memory read
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 9: 7. Mapping & Dataflow
Loop Optimization
Reordering
Tiling
Unrolling
Y. Ma et al., Optimizing the Convolution Operation to Accelerate Deep Neural Networks on FPGA

## Slide 10: 7. Mapping & Dataflow
Example: 1D Convolution
y = F.conv1d(x)
Library Call
time
0
0
0
filter
input
output
1
1
0
2
2
0
3
3
0
1
0
1
1
2
3
2
3
4
1
1
1
2
0
2
1
2
3
3
4
5
2
2
2
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 11: 7. Mapping & Dataflow
Example: 1D Convolution
Where should we map the weights?
on-chip RAM, registers, or DRAM
What effect will this have on a cache size of 4?
Cache eviction and refetching multiple times
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)
Output (q) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 0 | 1 | ..
Input (w) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 2 | 3 | ..
Weight (s) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | ..
Notes: Input 12
Weight 4
Output 9
Input (w) : 0 1 2 3 4 5 6 7
Weight (s) : 0 0 0 0 0 0 0 0
Output (q) : 0 1 2 3 4 5 6 7

## Slide 12: 7. Mapping & Dataflow
Mapping: Dataflow Selection
?
?
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 13: 7. Mapping & Dataflow
Mapping: Dataflow Selection
Compiler can re-order loops without changing functionality
Compiler heuristics can model the approximate effect on runtime and memory access
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 14: 7. Mapping & Dataflow
Dataflow Choice (Loop reordering)
Loop reordering
Output (q) | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | ..
Input (w) | 0 | 1 | 2 | 3 | 1 | 2 | 3 | 4 | 2 | 3 | 4 | 5 | 3 | 4 | 5 | 6 | 4 | 5 | 6 | 7 | ..
Weight (s) | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | ..
Output (q) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 0 | 1 | ..
Input (w) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 2 | 3 | ..
Weight (s) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | ..
Notes: Input (w) : 0 1 2 3 4 5 6 7
Weight (s) : 0 0 0 0 0 0 0 0
Output (q) : 0 1 2 3 4 5 6 7
Input (w) : 0 1 2 3 1 2 3 4
Weight (s) : 0 1 2 3 0 1 2 3
Output (q) : 0 0 0 0 1 1 1 1

## Slide 15: 7. Mapping & Dataflow
Dataflow Choice (Loop reordering)
Example: 2D Convolution
MCUNet: Tiny Deep Learning on IoT Devices [Lin et al., NeurIPS 2020]
On-Device Training Under 256KB Memory [Lin et al., NeurIPS 2022]
Notes: C00 = a00*b00 + a01*b10 + a02*b20
C01 = a00*b01 + a01*b11 + a02*b21
…
C00 += a00*b00, C01 += a00*b01, C02 += a00*b02
C00 += a01*b10, C01 += a01*b11, C02 += a01*b12

## Slide 16: 7. Mapping & Dataflow
Loop Tiling
Choose a tile size on which to operate
  Practically: Break a loop into 2 loop
  Can break into multiple loops, each can be mapped hierarchically onto a memory system
Tiling
Size of a tile
Number of tiles
DRAM
SRAM
registers
Example: hierarchical tiling
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)
Output (q) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 0 | 1 | ..
Input (w) | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 1 | 2 | ..
Weight (s) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | ..
q1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ..
q0 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | ..
Output (q) | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | ..
Input (w) | 0 | 1 | 2 | 3 | 1 | 2 | 3 | 4 | 2 | 3 | 4 | ..
Weight (s) | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | ..
Notes: Q: output 8개
Q1: 2개 tile
Q0: 4개/tile

## Slide 17: 7. Mapping & Dataflow
Loop Tiling
Example: 2D Convolution
Adapted from “TinyML and Efficient Deep Learning Computing” Lecture (Fall 2024) by Prof. Song Han (MIT)

## Slide 18: 7. Mapping & Dataflow
Loop Unrolling
Overheads of loop control
  Arithmetic operations for pointers (e.g., i, j, k)
  End of loop test (e.g., k < N)
  Branch prediction
Reducing the overheads by loop unrolling
  Replicate the loop body a number of times
  Tradeoﬀ between binary size and reduced overheads
Adapted from “TinyML and Efficient Deep Learning Computing” Lecture (Fall 2024) by Prof. Song Han (MIT)

## Slide 19: 7. Mapping & Dataflow
Loop Unrolling
Adapted from “TinyML and Efficient Deep Learning Computing” Lecture (Fall 2024) by Prof. Song Han (MIT)

## Slide 20: 7. Mapping & Dataflow
Loop Unrolling
Y. Ma et al., Optimizing the Convolution Operation to Accelerate Deep Neural Networks on FPGA

## Slide 21: 7. Mapping & Dataflow
Vectorization
Parallelize operations within your smallest tile
  Not possible without tiling!
Tiling mainly done to fit the data in various parts of the memory hierarchy
Vectorizing the smallest tile is done to leverage hardware parallelism
Vectorization
Size of a tile
Number of tiles
Tiled
Tiled + Vectorized
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)
Notes: • 원래 구조: innermost loop가 q0에 대해 돌면서 s는 고정. 이 경우, i[w]는 q0에 따라 연속적일 수 있지만, f[s]는 스칼라값으로 남아있어 벡터화에서 모든 루프 변수가 연속적으로 변하는 장점을 충분히 활용하지 못할 수 있습니다.
• 변경된 구조: innermost loop가 s0에 대해 돌면서, s가 s1와 s0에 의해 연속적으로 증가합니다. 이로 인해 f[s]와 i[q+s]의 메모리 접근이 연속적이 되어, SIMD 벡터화의 이점을 극대화할 수 있습니다.

## Slide 22: 7. Mapping & Dataflow
Tiled + Vectorized
Tile size?
2
# PEs/Cores ?
Adapted from “Machine Learning Hardware and Systems” Lecture (Fall 2024) by Prof. M. Abdelfattah (Cornell Tech)

## Slide 23: 7. Mapping & Dataflow
Edge-Cloud Collaborative Inference
Limited resources
Energy
TX bandwidth
Goal:
Partition DNN inference for
minimum energy and maximum throughput at the edge platform
Edge platform
Cloud platform
Wireless
TX
‘car’
[1] J. H. Ko et al., Edge-Host Partitioning of Deep Neural Networks with Feature Space Encoding for Resource-Constrained Internet-of-Things Platforms, AVSS 2018
[2] M. F. Amir, J. H. Ko et al., 3-D Stacked Image Sensor With Deep Neural Network Computation, IEEE Sensors Journal, 2018
[3] B. A. Mudassar, J. H. Ko et al., Edge-cloud collaborative processing for intelligent internet of things: a case study on smart surveillance, DAC 2018

## Slide 24: 7. Mapping & Dataflow – Collaborative Inference
Three Inference Approaches to Edge-Cloud Collaboration
Wireless TX
‘car’
Edge platform
Cloud platform
Entire inference at the cloud
Entire inference at the edge
‘car’
‘car’
Decoding
Encoding
Intermediate
feature
Edge-cloud partitioned inference
‘car’

## Slide 25: 7. Mapping & Dataflow – Collaborative Inference
Tradeoff between Computation/Memory & Transmission
Chart: Computation (Mega ops)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Computation (cumulative) | 0 | 100.5318 | 527.6802 | 670.274 | 884.1646 | 1026.7583 | 1062.7583 | 1078.7583 | 1082.6646
Memory access (cumulative) | 0 | 0.066467 | 0.28348 | 0.82784 | 1.1794 | 1.4276 | 6.3255 | 13.5982 | 15.1301
Chart: Layer #
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Transmission | 0.28711 | 0.13348 | 0.08252 | 0.12378 | 0.12378 | 0.017578 | 0.0078125 | 0.0078125 | 0.0019073
Input
conv1
conv2
conv3
conv4
conv5
fc6
fc7
fc8
More layers at edge
-> Computation/
memory demand ↑
-> Transmission demand ↓
(Analysis with AlexNet)
Layer to partition
Host inference
Edge inference

## Slide 26: 7. Mapping & Dataflow – Collaborative Inference
Fine Tuning of Partitioned Network
Chart: Compression ratio
| 67.5 | 33 | 23 | 19.149999999999999 | 17.5 | 14
Fine-tuned | 0.059 | 0.021 | 0.01 | 0.001 | 0.002 | 0
Original | 0.054 | 0.022 | 0.014 | 0.005 | 0.004 | 0
QF=30
QF=35
QF=40
Encoding with range of QF for target accuracy
…
Original
output feature
conv1
fc6
fc7
fc8
Fine tuning
Partitioned network at the host platform
conv5
Encoded
output feature
output feature
Target accuracy
Fine tuning of a partitioned network with encoded intermediated features
→ enhance compression performance
11% increase

## Slide 27: 7. Mapping & Dataflow – Collaborative Inference
Throughput/Energy Analysis
Chart: Throughput (frames/s)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Inference | 716.1915 | 136.4463 | 107.4188 | 81.4328 | 70.1236 | 45.5283 | 29.9371 | 27.923
Transmission | 4.2383 | 14.6612 | 35.196 | 29.098 | 34.6437 | 369.806 | 1357.2173 | 1281.7153 | 4510.3753
System | 4.2383 | 14.6612 | 35.196 | 29.098 | 34.6437 | 70.1236 | 45.5283 | 29.9371 | 27.923
Chart: Layers processed at edge
Computation | 0.10053 | 0.52768 | 0.67027 | 0.88416 | 1.0268 | 1.0628 | 1.0788 | 1.0827
Memory | 0.010635 | 0.045357 | 0.13245 | 0.1887 | 0.22841 | 1.0121 | 2.1757 | 2.4208
Encoding | 0.12701 | 0.059049 | 0.036504 | 0.054756 | 0.054756 | 0.007776 | 0.003456 | 0.003456 | 0
Transmission | 22.9453 | 6.5785 | 2.7112 | 3.2535 | 2.7112 | 0.24752 | 0.064171 | 0.068449 | 0.019789
Input
conv1
conv2
conv3
conv4
conv5
fc6
fc7
fc8
Min. system energy & Max. system throughput @ end of conv layers
Energy
Throughput

## Slide 28: 7. Mapping & Dataflow – Collaborative Inference
Throughput/Energy Advantages
Chart: Energy efficiency (Frame/J)
| 234.9444181971603
 | 27.923
Inference at host | 4.2957
 | 70.1236
Inference
at edge
Inference
at cloud
Partitioned
inference
2.3x throughput ↑
2.5x E efficiency ↑
15.3x throughput ↑
16.5x E efficiency ↑

## Slide 29: 7. Mapping & Dataflow – Collaborative Inference
Analysis on Network type
VGG-16
ResNet-50
Chart: Energy efficiency (Frames/J)
| 117.5875198699796
 | 24.0255
 | 24.946
 | 4.3537
Chart: Energy efficiency (Frames/J)
| 50.921497726842091
Inference at edge | 2.0636
Partitioned inference with feature encoding | 8.7964
Inference at host | 5.2245
Edge
Cloud
Partitioned
Edge
Cloud
Partitioned
Large FC layers → entire at cloud than edge
Deep conv layers + one FC layer → entire at edge than host
Partitioned inference is better than entire cloud or edge inference

## Slide 30: 7. Mapping & Dataflow – Collaborative Inference
Analysis on Transmission Channel
Chart: Energy efficiency (Frame/J)
| 282.86089439447102
Inference at edge | 27.923
Inference at host | 2.162
Partitioned inference with feature encoding | 70.1236
Chart: Energy efficiency (Frame/J)
| 284.19203506231202
 | 27.923
 | 41.6106
 | 70.1236
Edge
Cloud
Partitioned
Edge
Cloud
Partitioned
Low BW (1 Mbps)
High BW (22 Mbps)
BW ↑ → cloud inference performance ↑
Partitioned inference outperforms for both BW

## Slide 31: 7. Mapping & Dataflow – Collaborative Inference
Analysis on Transmission Channel
Chart: TX energy (nJ/bit)
| 0 | 0.3 | 5.8 | 13 | 210 | 1520
 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
 | 22 | 5 | 0.22 | 0.035
host
conv1
conv2
conv5
fc6
edge
conv1
conv2
conv5
fc6
edge
Bluetooth (@2Mbps)
Wifi (@22Mbps)
Bluetoogh low-energy (@ 1Mbps)
Wifi (@1Mbps)
Partitioning layer for min energy
Partitioning at
last conv layer (conv5)
covers wide range of TX models
Partitioning layer for max throughput

## Slide 32: 7. Mapping & Dataflow – Collaborative Inference
Partitioning of OD (YOLO) Models
YOLO v2 architecture imposes difficulties for partitioning
  Input of a layer after the split point may depend on the multiple previous layers
Entire edge or cloud inference is still better
W. Magalhães et al., Evaluating Edge-Cloud Computing Trade-Offs for Mobile Object Detection and Classification with Deep Learning, Journal of Information and Data Management, 2020

## Slide 33: 7. Mapping & Dataflow – Collaborative Inference
Image
Backbone
Neck
Edge
Cloud
BBOXs / Labels
Image
Backbone
Neck
BBOXs / Labels
Edge
Cloud
Feature Reconstruction with Asymmetric Scaling
Feature
reconstruction
network
<Baseline structure>
<Proposed structure>
Asymmetric scaling

## Slide 34: 7. Mapping & Dataflow – Collaborative Inference
Feature Reconstruction with Asymmetric Scaling
Chart: 
| Edge only | Cloud only | Partition-base | Ours-performance | Edge only | Cloud only | Partition-base | Ours-performance | Edge only | Cloud only | Partition-base | Ours-performance | 5 | 10 | 20
Edge Inference | 86.2 | 0 | 48.5 | 34.6 | 86.2 | 0 | 48.5 | 34.6 | 86.2 | 0 | 48.5 | 34.6
Edge Compression | 0 | 17.17 | 17.17 | 2.17 | 0 | 17.17 | 17.17 | 2.17 | 0 | 17.17 | 17.17 | 2.17
Transmission | 0 | 144 | 156 | 7.16 | 0 | 72 | 78 | 3.58 | 0 | 36 | 39 | 1.79
Cloud Processing | 0 | 16.22 | 7 | 13.51 | 0 | 16.22 | 7 | 13.51 | 0 | 16.22 | 7 | 13.51
Latency (ms)
Partitioned (baseline)
Partitioned (proposed)
Partitioned (baseline)
Partitioned (proposed)
Partitioned (baseline)
Partitioned (proposed)
5Mbps
10Mbps
20Mbps
34
J. C. Lee, Y. Kim, S. Moon and J. H. Ko, "A Reconfigurable Neural Architecture for Edge–Cloud Collaborative Real-Time Object Detection," in IEEE Internet of Things Journal, 2022, doi: 10.1109/JIOT.2022.3205682.

## Slide 35: 7. Mapping & Dataflow – Collaborative Inference
Intermediate Feature Transmission
Feature transmission is lossy
  Due to bit error, packet loss, …
Solutions
  Optimal partition point search under lossy environment
  Feature loss recovery
  Loss-augmented training
Kim H, Choi JS, Kim J, Ko JH. A DNN partitioning framework with controlled lossy mechanisms for edge-cloud collaborative intelligence. Future Generation Computer Systems. 2024 May 1;154:426-39.

## Slide 36: Thank you!
Lecture 6: Polling and Interrupt
Questions or comments?
Jong Hwan Ko
SungKyunKwan University, Korea
Department of Information and Communication Engineering
jhko@skku.edu